## Slide 1: (Raspberry) Pi Day
3/2/24
ORION

## Slide 2: Goals for Today…
Learn about single board computers (SBC) -namely, the Raspberry Pi board
  Background
    What can they do?
    How are they used?
    How much do they typically cost $ ?
      Arduino versus Raspberry P
  Learn about enabling the technologies…
    Linux operating system,
    IoT (Internet-of-things)
    Introduction to computer programming…
      Making hardware and software talk:
        Network protocols: MQTT and HTTP (Web sockets)
  Develop Hands on project: You will use the Raspberry Pi 3 to construct a custom IoT Device: Build Smart” (IoT) light bulb from scratch
    Ingredients?
      A Raspberry PI 3B, electronic components, and an ordinary desktop
        You build the software to make it work!

## Slide 3: Project: IoT “Smart” Light Bulb Prototype
MQTT Broker on RPi
Python
Backend
Bulb/”on”
Bulb/”off”
Publish in topic: Bulb/
MQTT over Websockets
Bulb Web app: (based on HTML 5 CSS and JavaScript)
Message: “on”/”off”
Subscribe to topic: Bulb/
Python smart bulb logic running on RPi

## Slide 4: Project: Develop an IoT “Smart” Light Bulb Prototype using an ordinary desk lamp
Build the device:
  Module 1: Provisioning the Raspberry Pi for Use
    Write the operating system image, configure services
      Raspberry Pi OS, SSH, VNC
  Module 2:
  Module 3:
  Design and implement an electronic circuit required to remotely control the lamp
    Develop the software to control the lamp using the raspberry pi connected to the device (electronic circuit) using the GPIO (general purpose input/output) header
  Design and implement the web based (front-end) interface software, enabling the user interact with the light bulb
Use MQTT protocol to make the software and hardware communicate.
  https://mqtt.org/

## Slide 5: Background
What is a Raspberry PI?
  https://www.youtube.com/watch?v=eZ74x6dVYes
    Pi board comparison: https://socialcompare.com/en/comparison/raspberrypi-models-comparison
      Uses? Many!
        industrial automation
          applications for prototyping
          embedded systems
          low-cost process controller
        Home automation
          DIY, education
  Raspberry Pi versus Arduino
    https://webbylab.com/blog/arduino-vs-raspberry-pi-key-differences-comparison-table/
      https://www.youtube.com/watch?v=p40OetppIDg
  Raspberry Pi 5 (latest version)
      https://www.raspberrypi.com/news/introducing-raspberry-pi-5/

## Slide 6: Project Goal: IoT “Smart” Light Bulb Prototype
MQTT Broker on RPi
Python
Backend
Bulb/”on”
Bulb/”off”
Publish in topic: Bulb/
MQTT / Web sockets
Bulb Web app: (based on HTML 5 CSS and JavaScript)
Message: “on”/”off”
Subscribe to topic: Bulb/
Python smart bulb logic running on RPi

## Slide 7: Module 1: Provisioning the Raspberry Pi for Use
Write the operating system image: Raspberry Pi OS
Configure services:
  Secure Shell (SSH)
    Run: raspi-config
    I2C
    Virtual Network Computing (VNC)

## Slide 8: Install and Configure the Operating System (OS) and Services
Download and Install Raspberry Pi OS using Raspberry Pi Imager
  https://www.raspberrypi.com/software/
  Insert micro-SD card into USB card reader and run the imager tool. See screen shots below

## Slide 9: Write the Operating System (OS) Image to the SD card
2. Choose OS: Select Pi OS (32 bit) with desktop env.
3. Storage location: Select the micro- SD card from USB reader
1. Raspberry Pi device: select your version (Pi 3)

## Slide 10: Before you proceed, Make sure….
1. Raspberry Pi 3 is selected
2. 32-bit Legacy OS w/ desktop environment
3. Make sure the micro-SD card is selected as the storage
* Only when 1,2, and 3 are verified, click “next”

## Slide 11: Customize the Settings:
Click “Edit Settings”

## Slide 12: Important! Perform the next steps with the mentor
Follow the instructions as specified, or your Raspberry Pi will not be configured properly for the “smart’ bulb project
Proceed to the next slide to begin

## Slide 13: These settings must be as specified, or your Pi will not be properly configured for the project
Specify the hostname. Use your Team name with “pi” appended. For example, Team “Viper”, would use hostname “viperpi” as shown
Configure the WIFI settings to use the Griffiss institute Guest network.
Set the username to “pi” and the
Password to “team chooses” (don’t share)
Select the country to ‘US’ and set the locale settings as illustrated
Click “Save”

## Slide 14: Customize the Settings:
Click “Edit Settings”

## Slide 15: Enable Secure Shell
1. Click “Services” Tab
2. Choose password authentication
3. Save settings

## Slide 16: Customize the Settings:
1. Click “Yes”
2. Click “Yes” to write the operating system image

## Slide 17: Wait for the OS image to be written to SD-card

## Slide 18: Start an SSH session with the Raspberry Pi
Open a new terminal window
Type command: pi@teamnamepi.local
Replace “teamname” with name of your Team
Example: Team “Viper”
ssh pi@viperpi.local
Type command: yes
Congratulations. You have a new (remote) connection the Raspberry Pi

## Slide 19: Run the Raspberry Pi configuration tool to configure the services
Type command: sudo raspi-config

## Slide 20: Select Configure the Interfaces:
Select menu item 3:

## Slide 21: Enable SSH, VNC, and I2C
SSH is already enabled
Enable both VNC and I2C
I2C (Inter-Integrated Circuit) is widely used a serial bus protocol for establish serial communication integrated circuits (ICs)
Select Finish to exit

## Slide 22: Setup VNC viewer laptop PC
VNC stands for Virtual Network Computing. It is a cross-platform screen sharing system that was created to remotely control/view another computer
  Download the VNC viewer application to Windows (host) computer:
    https://www.realvnc.com/en/connect/download/viewer/

## Slide 23: Establish a VNC session with Raspberry PI
Open the Real VNC viewer and enter the Raspberry Pi host name in the connect box.
  recall the host have given should be the team's name followed by the keyword word “pi”.
    For example, for Team “Viper”, the raspberry pi host name should be “viperpi.local”
    Enter the hostname for your team’s pi in the Real VNC viewer connect box as shown and press
    Supply the username “pi”, and the password your team specified.

## Slide 24: Example established VNC session Remote desktop experience, without the need for a physical monitor and peripherals
Questions / Recap ?
Source: http://web.mit.edu/cdsdev/src/howitworks.html

## Slide 25: MQTT enables communication between the web (user) interface and the Raspberry PI device (the electronic circuit)
MQTT stands for Message Queuing Telemetry Transport) -is a simple messaging protocol, designed for constrained devices with low bandwidth. – [1]
    perfect for exchanging data between IoT devices.
  https://mqtt.org/
  https://learn.sparkfun.com/tutorials/introduction-to-mqtt/all
  https://www.geeksforgeeks.org/introduction-of-message-queue-telemetry-transport-protocol-mqtt/ - [1]
  https://www.geeksforgeeks.org/fundamental-features-of-mqtt/
  https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/
  MQTT over web sockets (JavaScript) tutorial
    http://www.steves-internet-guide.com/using-javascript-mqtt-client-websockets/
Source: https://www.geeksforgeeks.org/introduction-of-message-queue-telemetry-transport-protocol-mqtt/ - [1]

## Slide 26: IoT “Smart” Light Bulb
MQTT Broker on RPi
Python
Backend
Bulb/”on”
Bulb/”off”
Publish in topic: Bulb/
MQTT over Websockets
Bulb Web app: (based on HTML 5 CSS and JavaScript)
Message: “on”/”off”
Subscribe to topic: Bulb/
Python smart bulb logic running on RPi

## Slide 27: Install Mosquitto MQTT Broker on Raspberry PI
Start an SSH session with the Raspberry Pi:
  Open a command terminal
    Enter command: ssh pi@{teamname}pi.local - replace {teamname} with corresponding team name: example Team: “Viper”  ssh pi@viperpi.local
    From the ssh session, enter command:
      sudo apt install -y mosquitto mosquitto-clients
    To make Mosquitto auto start when the Raspberry Pi boots, you need to run the following command (this means that the Mosquitto broker will automatically start when the Raspberry Pi starts):
      sudo systemctl enable mosquitto.service
    Test the installation by running the following command:
      mosquitto -v
Source: https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/

## Slide 28: MQTT Broker configuration: Websockets
Configure the MQTT Broker to use Web sockets
  https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/
  http://www.steves-internet-guide.com/mqtt-websockets/
Start (or use existing) SSH session with the Pi
  Use nano or vi to open the configuration file: sudo nano /etc/mosquitto/mosquitto.conf
Append the highlighted configuration and save
Restart the service: sudo systemctl restart mosquitto
listener 1883
listener 9001
protocol websockets
allow_anonymous true

## Slide 29: Interlude: Short Linux Primer
Wait! Isn’t this camp about Raspberry Pi? Why are we pausing to talk about Linux?
  Ans: Linux is an operating system that runs almost everywhere! In almost all IT technical careers, you will be required to know and use Linux proficiently.
    Linux runs in more environments than you may realize:
      Big enterprise datacenters, Cloud service backends, your Android phone, smart TVs, cameras, wearables (smart watches), etc.
        And yes… it is the default OS that runs on your Raspberry PI.
          Called Raspberry PI OS (based on the Debian GNU/Linux distribution )
            https://en.wikipedia.org/wiki/Raspberry_Pi_OS
Reasonable (Funny) Video Intro to Linux
  https://www.youtube.com/watch?v=zA3vmx0GaO8

## Slide 30: Linux Command Line
Shell - CLI - primer user interface to operating. Its essentially a program interprets user commands, and run other programs
Understanding the Filesystems
  Files and folders (called directories), and are organized hierarchically (in a tree structure)
Basic Linux Commands (video)
  https://www.youtube.com/watch?v=bb_ApuH15YE
Further study reference: “The Linux Command line” ebook
  https://linuxcommand.org/tlcl.php
ls – list contents of folder
~ refers to home folder
cd – change to new directory (folder)

## Slide 31: Module 2: Prototyping the IoT “Smart bulb” device
The “smart bulb” hardware is implemented as a simple electronic circuit, consisting of the following components:
  List of components:
    1 x Raspberry Pi 3B
    1 x full size bread board
    1 x 40-pin ribbon cable
    1 x T-cobber GPIO extender
    2 x 220 Ohm resistor
    2 X 5mm LED
    1 X 5v 1 channel relay
    Jumper wires
    Switch button

## Slide 32: 40-pin GPIO (general purpose input/output) Header Overview
Allows the code running on Raspberry PI to interface with the outside world…
  Supports digital communication with external devices (the outside world) using serial bus protocols including: UART, SPI, i2c
    Does NOT support analog inputs
      We can easily fix by connecting an analog-to-digital converter (ADC)
https://learn.sparkfun.com/tutorials/introduction-to-the-raspberry-pi-gpio-and-physical-computing/gpio-pins-overview
https://www.raspberrypi-spy.co.uk/2012/06/simple-guide-to-the-rpi-gpio-header-and-pins/
https://projects.raspberrypi.org/en/projects/physical-computing/1
40-pin GPIO header
Pin numbering: Board, BCM/GPIO/WiringPi

## Slide 33
Brief Review of Electronic Components

## Slide 34: Breadboard
The breadboard is organized in rows and columns called socket strips (shown in cyan)
  Socket strips are connected vertically
The bus strips on the edges (shown in red) are using connecting a power source (3.3v and 5v for the Pi)
  Edge strips connect horizontally over the length of the breadboard
Socket strips allow components to be connected without soldering or wires. [2]
Any pin plugged into row 1, column ‘a’ would be connected to any pin plugged into row 1, columns ‘b-e’.
On the other side of the divider, row 1 columns f-j are similarly connected. [2]
Source: https://learn.microsoft.com/en-us/training/modules/create-iot-device-dotnet/2-construct-iot-hardware - [2]

## Slide 35: 5v Relay Board Relay Module 1 Channel
  An electromagnetic switch used to programmatically activate/deactivate external devices (i.e., a desk lamp or fan).
  Use a small current to control separate (often larger) current.
    When a small current is passed through the low-voltage (5v DC) input on the relay it activates the switch (using a coil) and completes the separate high voltage (120v AC) circuit (i.e., a larger current).
      This is one way we how can control external devices: fans, desk lamps

## Slide 36: Resistor
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element. In electronic circuits, resistors are used to reduce current flow, adjust signal levels, to divide voltages – [3]
[3] - https://en.wikipedia.org/wiki/Resistor
Use of 220 Ohm resistor to limit the current through the LED and to prevent excess current that can burn out the LED

## Slide 37: LED and Button Switch
The longer leg (known as the ‘anode’), is always connected to the positive supply of the circuit. The shorter leg (known as the ‘cathode’) is connected to the negative side of the power supply, known as ‘ground’.
LED stands for Light Emitting Diode, and glows when electricity (current) is passed through it. - [2]
Connect one side of the switch to an input pin on the Raspberry Pi, in this case we use pin 10.
The other side of the switch we connect to 3.3V on pin 1 using a resistor.
  The resistor is used as a current limiting resistor to protect our input pin by limiting the amount of current that can flow. [3]
Source: https://raspberrypihq.com/use-a-push-button-with-raspberry-pi-gpio/ - [3]
Source: https://thepihut.com/blogs/raspberry-pi-tutorials/27968772-turning-on-an-led-with-your-raspberry-pis-gpio-pins - [2]

## Slide 38: “Smart” bulb device (Fritzing circuit design) concept
  Fritzing is an open-source hardware initiative that makes electronics accessible as a creative material for anyone.
    https://fritzing.org/

## Slide 39: Completed “Smart” bulb device (hardware prototype)

## Slide 40: “Smart” bulb device (concept versus prototype)
versus

## Slide 41: Attach the T-Cobbler (GPIO expander to the breadboard)
** Note the orientation to negative/positive (power) terminal strips
*** Insert the t-cobbler beginning in the first column of sockets in the breadboard
* Note of the rows on exposed on each side of the t-cobbler (3 on one side, and 2 on the other. Your design should look like this too.

## Slide 42: Construct the device (electronic circuit):
Connect a “Red” jumper wire to the 3.3v pin of the T-Cobber and the positive (+) terminal strip of the breadboard (same side as the 3v pin). This provides 3.3v power to entire edge terminal socket strip designated by the red line
Connect a “Black” jumper wire to a “GND” pin on 3.3v side of the T-Cobbler, and the negative (-) terminal strip on the breadboard (same side 5v pin). This provides a ground (-) to the entire edge terminal socket strip designated by the blue line
Push a switch button onto the bread board (as shown). Connect an “Green” wire to GPIO 23 from the T-cobbler to the output side of the button
Connect “Red” wire from the positive (+) 3.3v terminal strip of the breadboard to the input side of the switch button
Push an LED into the breadboard (as shown). Note: the bend in the LED terminal indicates the longer (+) LED anode. Connect a 220-ohm resistor between LED cathode (shorter negative - ) pin and the negative (-) terminal strip on the breadboard
Connect a “Yellow” wire from the output side of the switch button to the longer (+) LED anode terminal of the LED
Push an LED into the breadboard (as shown). Note: the bend in the LED terminal indicates the longer (+) LED anode. Connect a 220-ohm resistor between LED cathode (shorter negative - ) pin and the negative (-) terminal strip on the breadboard
Connect a “Blue” jumper wire to the GPIO pin 23 from the T-cobbler, and the IN terminal of the 3.3v 1 channel relay
Connect a “Red” jumper wire from 3.3v positive (+) terminal strip of the breadboard to VCC terminal on of the relay
Connect a “Black” jumper wire from negative (+) terminal strip of the breadboard to GND terminal on of the relay
Connect a “Red” wire to the NO (Normally open) terminal of the relay to the 3.3v (positive +) terminal strip of the breadboard
Connect “Red” wire the COM (Common) terminal of the relay to the (positive +) terminal of the LED
1.
2.
4.
*5.
*7.
3.
6.
8.
9.
10.
11.
* - indicates multiple steps
Power off and disconnect the Raspberry Pi power source
Connect and power on Raspberry Pi and test by press the button to activate the bulb
12.

## Slide 43: Module 3: Develop the software to control the “smart” bulb
MQTT Broker on RPi
Python
Backend
Bulb/”on”
Bulb/”off”
Publish in topic: Bulb/
MQTT / Web sockets
1. Smart Bulb Web app: (based on HTML 5 CSS and JavaScript)
Message: “on”/”off”
Subscribe to topic: Bulb/
2. Python smart bulb logic running on RPi
Develop the backend to control the lamp
Develop the frontend user interface

## Slide 44: Download the smart bulb source code from GitHub: https://github.com/mwcorley79/smartbulb
Choose “Code””Download Zip”, and save the zip to the “Desktop” folder on the laptop
Navigate to Desktop, and right-click the zip file, and choose extract all

## Slide 45: Project structure: navigate to extracted folder to view the project files
smart_bulb.html – This is front-end html (html-based ) user web interface
smart_bulb.py – This is the back-end Python script that runs on the Raspberry Pi
  Communicates with the GPIO header to control the desk lamp

## Slide 46: Install Visual Studio Code (VSCode) Editor
  VSCode is the most popular software development code editor available today.
    Typically, the software development for the Raspberry Pi is performed on a development host (your windows laptop) which equipped with development tools including: VSCode, Python, debuggers, and potentially device simulators etc.)
      Software is typically developed and tested incrementally
        The resulting software artifacts are moved from the dev host to the Raspberry Pi (sometimes referred to as the target device) and tested.
          Debuggers help with development
            Note: although development can be performed directly on the Raspberry Pi, this is more often performed on the dev host
  Download and install Visual studio code for Windows:
    https://code.visualstudio.com/download

## Slide 47: Opening the Project in VSCode
Navigate to the Desktop
Double click the VSCode icon to start the editor
Choose “Open Folder”, select the project folder, and click “Select Folder”

## Slide 48: The back-end (Python) code in VSCode: smart_bulb.py
The back-end (Python 3) script runs on the Raspberry Pi to control the desk lamp
  We need to copy smart_bulb.py to the Raspberry Pi using secure copy (SCP)
Controlling the lamp requires logic that uses
  Paho MQTT library to connect to the broker using MQTT over web sockets
    subscribes to the “bulb” topic, and receives “on” / “off” messages
  Message processing logic uses a GPIO access library to interface with of the desk lamp by controlling the relay switch
Take a few mins to review this code

## Slide 49: Create folder on the Raspberry Pi to store smart_bulb.py
  Open windows terminal and start an SSH session with Raspberry Pi:
      Enter command: ssh pi@{teamname}pi.local - replace {teamname} with corresponding team name:
        Example Team: “Viper”  ssh pi@viperpi.local
        Create a new destination folder to store the smart_bulb.py script
            mkdir ~/smartbulb
        You can type exit to terminate the SSH session, but leave it active, we will continue to use it

## Slide 50: Use Secure (SCP) to copy smart_bulb.py to Raspberry Pi
  Navigate to the project folder, right-click, and choose “Open in terminal
  Type the following command:
    scp .\smart_bulb.py pi@teamnamepi.local:~/smartbulb
      This copies smart-bulb.py to the Raspberry Pi destination folder created in the previous step: ~/smartbulb
      Replace pi@{teamname}pi.local - with corresponding team name:
        Example Team: “Viper”  pi@viperpi.local
  Example:

## Slide 51: Install the Python dependencies required to run smart_bulb.py
Return to active SSH session with the Raspberry Pi (or start a new session)
  Navigate the folder created previously for storing the smart_bulb.py
    Enter command: cd ~/smartbulb
  Verify the smart_bulb.py was successfully transferred by entering command: ls –l
  The IoT smartbulb project was developed to be compatible with Python 3.9 and greater:
    Verify Python 3 is preinstalled on the Raspberry Pi
      python3 –version
    Install Paho MQTT Client package library
      pip3 install "paho-mqtt<2.0.0"
        Note: Version 2.0.0 of the library was released in February 2024; and contains breaking changes so the above installs v1
    Install Python module to control the GPIO: RPi.GPIO
      pip3 install RPi.GPIO

## Slide 52
smart_bulb.py
”on”, ”off”
Subscribe to MQTT
topic: Bulb/
Messages:
Paho MQTT client
WebSocket
(port 9001)
RPi.GPIO
Relay (Lamp) signal on / off
MQTT Broker
To Run, enter command:
python ./smart_bulb.py
Back-end: smart_bulb.py (operational concept)

## Slide 53: Front-end user interface (HTML/JS) code in VSCode: smartbulb.html
The web interface allows the user to toggle a slider switch button that simulates turning a lightbulb from positions.
  Uses MQTT over web sockets to control the operation of a desk lamp

## Slide 54: Front-end user interface (HTML/JS) code: smartbulb.html
Find the variable “host” on line 105
Replace the value: “[ip-address]” with the IPv4 address of the Raspberry Pi and save the file.
To find the IP address, open a terminal and SSH to the Raspberry Pi
  run the following command: ifconfig
The ip address is shown under the wireless network interface (wlan0)
Change line 105 to the IP address issues to the Pi.
For Example:
let host = “192.168.1.10”
Save the file
Smartbulb.html is developed using a combination web technologies: HTML 5, CSS , and JavaScript
A JavaScript library is used to establish MQTT connectivity with an MQTT Broker over Websockets

## Slide 55: Serve up the user interface in a browser such Chrome or Firefox
Open a browser, navigate to the smartbulb project folder and open smartbulb.html

## Slide 56: Test the Smart bulb: Make sure the back-end: smart-bulb.py is running
Enter Team name and click “submit”
Toggle the light switch on/off to control the light bulb
Front-end user interface (HTML/JS) code in VSCode: smartbulb.html

## Slide 57: Challenge Questions…
Can you change your front-end code, so it controls the instructor’s desk lamp at the front of the room?
  You’ll need one piece of the information to accomplish this.
Can you modify your front-end code to control another team’s lightbulb?
Would you say that your IoT desk lamp implementation meets a reasonable level of security? Why or why not?
Notice (on line 28) that your back-end code (smart_bulb.py) connect to the MQTT over local host (127.0.0.1) .
  Explain what local host is?
  Why can your back-end code connect to MQTT over local host?
What is your most surprising discovery about the Raspberry Pi?

## Slide 58: Raspberry Pi Edge Processing : (AI Image Recognition Demo) (Time Permitting)
Object Classifier (External) Client – running on Windows 11
Object Classifier (REST) Service
HTTP-REST

## Slide 59: Where do you go from here?
Other STEM camps
Online based learning resources
  https://randomnerdtutorials.com/getting-started-with-raspberry-pi/
  Let's Learn .NET - IoT (Internet of Things) (youtube.com)
High school course work
  Computer Science/Programming/Cyber security
  College careers
    Computer Science, Computer/Electrical Enginneering

## Slide 60: That’s all Folks
Thank you for joining us for Pi Day!!

## Slide 61: Links (remove later)
https://www.raspberrypi.com/for-home/
https://www.raspberrypi.com/for-in
https://www.youtube.com/watch?v=eZ74x6dVYes
https://www.youtube.com/watch?v=p40OetppIDg
https://socialcompare.com/en/comparison/raspberrypi-models-comparison
3:22 and 14:30