## Slide 1: (Raspberry) PI Day
3/2/24
ORION

## Slide 2: Agenda for Today…
Learn about single board computers (SBC)
  What can they do? What are they used for? How much do they typically cost? $
    Discuss Arduino versus Raspberry Pi? Differences?
  Learn about enabling the technologies…
    Linux OS,
    IoT (Internet-of-things)
    Introduction to computer programming…
      Making hardware and software talk:
        Network protocols: MQTT and HTTP (Web sockets)
  Develop Hands on project: You will use the Raspberry Pi 3 to construct a custom IoT Device: Build “Smart” (IoT) light bulb from scratch
    Ingredients?
      A Raspberry PI 3B, and a few electronic components, and an ordinary desktop
        You build the software to make it work.

## Slide 3: The Prototype
MQTT Broker
Python
Backend
Bulb/message
Bulb/
MQTT / Web sockets
Web page:
html 5 / JavaScript

## Slide 4: Project: Develop an IoT “Smart” Light bulb from scratch
Develop the hardware:
  Design and implement an electronic circuit required to remotely control the operation of an ordinary table lamp
Develop the software
  Design and implement a web (front-end) user interface to drive a light bulb
  Design and implement electronic circuit (the IoT hardware) to control the lamp
    Use MQTT protocol to make the software and hardware communicate.

## Slide 5: Links
https://www.raspberrypi.com/for-home/
https://www.raspberrypi.com/for-in
https://www.youtube.com/watch?v=eZ74x6dVYes
https://www.youtube.com/watch?v=p40OetppIDg
https://randomnerdtutorials.com/getting-started-with-raspberry-pi/
https://socialcompare.com/en/comparison/raspberrypi-models-comparison
Let's Learn .NET - IoT (Internet of Things) (youtube.com) 3:22 and 14:30

## Slide 6: Module 1: Provisioning the Raspberry Pi for Use

## Slide 7: Install and Configure the Operating System (OS) and Services
Download and Install Raspberry Pi OS using Raspberry Pi Imager
  https://www.raspberrypi.com/software/
  Insert micro-SD card into USB card reader and run the imager tool. See screen shots below

## Slide 8: Write the Operating System (OS) Image to the SD card
2. Choose OS: Select Pi OS (32 bit) with desktop env.
3. Storage location: Select the micro- SD card from USB reader
1. Raspberry Pi device: select your version (Pi 3)

## Slide 9: Before you proceed, Make sure….
1. Raspberry Pi 3 is selected
2. 32-bit Legacy OS w/ desktop environment
3. Make sure the micro-SD card is selected as the storage
* Only when 1,2, and 3 are verified, click “next”

## Slide 10: Customize the Settings:
Click “Edit Settings”

## Slide 11: Important! Perform the next steps with the mentor
Follow the instructions as specified, or your Raspberry Pi will not be configured properly for the “smart’ bulb project
Proceed to the next slide to begin

## Slide 12: These settings must be as specified, or your Pi will not be properly configured for the project
Specify the hostname. Use your Team name with “pi” appended. For example, Team “Viper”, would use hostname “viperpi” as shown
Configure the WIFI settings to use the Griffiss institute Guest network.
Set the username to “pi” and the
Password to “team chooses” (don’t share)
Select the country to ‘US’ and set the locale settings as illustrated
Click “Save”

## Slide 13: Customize the Settings:
Click “Edit Settings”

## Slide 14: Enable Secure Shell
1. Click “Services” Tab
2. Choose password authentication
3. Save settings

## Slide 15: Customize the Settings:
1. Click “Yes”
2. Click “Yes” to write the operating system image

## Slide 16: Wait for the OS image to be written to SD-card

## Slide 17: Start an SSH session with the Raspberry Pi
Open a new terminal window
Type command: pi@teamnamepi.local
Replace “teamname” with name of your Team
Example: ssh pi@viperpi.local
Type command: yes
Congratulations. You have a new (remote) connection the Raspberry Pi

## Slide 18: Run the Raspberry Pi configuration tool to configure the services
Type command: sudo raspi-config

## Slide 19: Select Configure the Interfaces:
Select menu item 3:

## Slide 20: Enable SSH, VNC, and I2C
SSH is already enabled
Enable both VNC and I2C
I2C (Inter-Integrated Circuit) is widely used a serial bus protocol for establish serial communication integrated circuits (ICs)
Select Finish to exit

## Slide 21: Setup VNC viewer laptop PC
VNC stands for Virtual Network Computing. It is a cross-platform screen sharing system that was created to remotely control/view another computer
  Download the VNC viewer application to Windows (host) computer:
    https://www.realvnc.com/en/connect/download/viewer/

## Slide 22: Establish a VNC session with Raspberry PI
Open the Real VNC viewer and enter the Raspberry Pi host name in the connect box.
  recall the host have given should be the team's name followed by the keyword word “pi”.
    For example, for Team “Viper”, the raspberry pi host name should be “viperpi.local”
    Enter the hostname for your team’s pi in the Real VNC viewer connect box as shown and press
    Supply the username “pi”, and the password your team specified.

## Slide 23: Established VNC session: a remote desktop experience, without the need for physical monitor and keyboard/mouse peripherals

## Slide 24: MQTT Protocol is used to enable communication between the web (user) interface and the Raspberry PI
https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/

## Slide 25: Install Mosquitto MQTT Broker on Raspberry PI
SSH to the Raspberry Pi:
  Open a command terminal
    Enter command: ssh pi@{teamname}pi.local - replace {teamname} with corresponding team name: example Team: “Viper”  ssh pi@viperpi.local
    From the ssh session, enter command:
      sudo apt install -y mosquitto mosquitto-clients
    To make Mosquitto auto start when the Raspberry Pi boots, you need to run the following command (this means that the Mosquitto broker will automatically start when the Raspberry Pi starts):
      sudo systemctl enable mosquitto.service
    Test the installation by running the following command:
      mosquitto -v
Source: https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/

## Slide 26: MQTT Broker configuration
Configure the MQTT Broker to use Websockets
  https://randomnerdtutorials.com/how-to-install-mosquitto-broker-on-raspberry-pi/
  http://www.steves-internet-guide.com/mqtt-websockets/
  Use nano or vi to open: sudo nano /etc/mosquitto/mosquitto.conf
sudo systemctl restart mosquitto

## Slide 27: Interlude: Short Linux Primer
Wait! Isn’t this camp about Raspberry Pi? Why are we pausing to talk about Linux?
  Ans: Linux is an operating system that runs almost everywhere! In almost all IT technical careers, you will be required to know and use Linux proficiently.
    Linux runs in more environments than you may realize:
      Big enterprise datacenters, Cloud service backends, your Android phone, smart TVs, cameras, wearables (smart watches), etc.
        And yes… it is the default OS that runs on your Raspberry PI.
          Called Raspberry PI OS (based on the Debian GNU/Linux distribution )
            https://en.wikipedia.org/wiki/Raspberry_Pi_OS
Reasonable (Funny) Video Intro to Linux
  https://www.youtube.com/watch?v=zA3vmx0GaO8

## Slide 28: Linux Command Line
Shell - CLI - primer user interface to operating. Its essentially a program interprets user commands, and run other programs
Understanding the Filesystems
  Files and folders (called directories), and are organized hierarchically (in a tree structure)
Basic Linux Commands (video)
  https://www.youtube.com/watch?v=bb_ApuH15YE
Further study reference: “The Linux Command line” ebook
  https://linuxcommand.org/tlcl.php
ls – list contents of folder
~ refers to home folder
cd – change to new directory (folder)

## Slide 29: Module 2: Prototyping the IoT “Smart bulb” device
The “smart bulb” IoT device is implemented as a simple circuit, consisting of electronic components:
  Fritzing is an open-source hardware initiative that makes electronics accessible as a creative material for anyone.
    https://fritzing.org/
  List of components:
    1 x Raspberry Pi 3B
    1 x full size bread board
    1 x 40-pin ribbon cable
    1 x T-cobber GPIO extender
    2 x 220 Ohm resistor
    2 X 5mm LED
    1 X 5v 1 channel relay
    Jumper wires
    Switch button

## Slide 30: 40-pin GPIO (general purpose input/output) Header
Allows the software (code) to touch/control the outside world…
  Supports digital communication with external devices (the outside world) using serial bus protocols including: UART, SPI, i2c, and USB
    Does NOT support analog inputs
      We can fix that easily, by connecting an analog-to-digital converter (ADC) to Pi using serial communication
Serial comm Primer: https://www.youtube.com/watch?v=LEz5UCN3aHA

## Slide 31: Breadboard
The breadboard is organized in rows and columns called socket strips (shown in cyan)
  Socket strips are connected vertically
The bus strips on the edges (shown in red) are using connecting a power source (3.3v and 5v for the Pi)
  Edge strips connect horizontally over the length of the breadboard
Socket strips allow components to be connected without soldering or wires.
Any pin plugged into row 1, column ‘a’ would be connected to any pin plugged into row 1, columns ‘b-e’.
On the other side of the divider, row 1 columns f-j are similarly connected.
Source: https://learn.microsoft.com/en-us/training/modules/create-iot-device-dotnet/2-construct-iot-hardware

## Slide 32: 5v Relay Board Relay Module 1 Channel
  is an electromagnetic switch used to programmatically activate/deactivate external devices (i.e., a desk lamp or fan).
  Use a small current to control separate (often larger) current.
    When a small current is passed through the low-voltage (5v DC) input on the relay it activates the switch (using a coil) and completes the separate high voltage (120v AC) circuit (i.e., a larger current).
      This is one way we how can control external devices: fans, desk lamps

## Slide 33: Resistor
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element. In electronic circuits, resistors are used to reduce current flow, adjust signal levels, to divide voltages – [1]
[1] - https://en.wikipedia.org/wiki/Resistor
Use of 220 Ohm resistor to limit the current through the LED and to prevent excess current that can burn out the LED

## Slide 34: “Smart” bulb device (Fritzing circuit design concept)

## Slide 35: Completed “Smart” bulb device (hardware prototype)

## Slide 36: “Smart” bulb device (concept versus prototype)
versus

## Slide 37: Constructing the device (electronic circuit):
Connect a “Red” jumper wire to the 5v pin of the T-Cobber and the positive (+) terminal strip of the breadboard (same side as the 5v pin). This provides 5v power to entire edge terminal socket strip designated by the red line
Connect a “Black” jumper wire to a “GND” pin on 5v side of the T-Cobbler, and the negative (-) terminal strip on the breadboard (same side 5v pin). This provides a ground (-) to the entire edge terminal socket strip designated by the blue line
Push an LED into the breadboard (as shown). Note: the bend in the LED terminal indicates the longer (+) LED anode. Connect a 220-ohm resistor between LED cathode (shorter negative - ) pin and the negative (-) terminal strip on the breadboard
Connect a “Blue” jumper wire to the GPIO pin 23 from the T-cobbler, and the LED anode: (longer positive +) pin
Push a switch button onto the bread board (as shown). Connect an “Orange” wire to GPIO 24 from the T-cobbler to the input side of the button
Connect “Red” wire from the positive (+) 5v terminal strip of the breadboard to the input side of the switch button
Connect a “Red” jumper wire from 5v positive (+) terminal strip of the breadboard to DC+ terminal on of the relay
Connect a “Black” jumper wire from negative (+) terminal strip of the breadboard to DC- terminal on of the relay
Connect a “Yellow” jumper wire to the output side of the switch button to the IN1 terminal of the relay.
Push an LED into the breadboard (as shown). Note: the bend in the LED terminal indicates the longer (+) LED anode. Connect a 220-ohm resistor between LED cathode (shorter negative - ) pin and the negative (-) terminal strip on the breadboard
Connect a “Red” wire to the NO (Normally open) terminal of the relay to the 5v (positive +) terminal strip of the breadboard
Connect “Red” wire the COM (Common) terminal of the relay to the (positive +) terminal of the LED Note: the bend
1.
2.
4.
*5.
7.
*3.
*3.
*5.
*6.
8.
9.
*10.
11.
12.
* - indicates multiple steps
Power off and disconnect the Raspberry Pi power source
Connect and power on Raspberry Pi: press the button to activate the bulb

## Slide 38: Module 3: Develop the software to control the “smart” bulb
Prerequisites:
  Download and install Visual studio code for Windows:
    https://code.visualstudio.com/download

## Slide 39: Download the smart bulb source code from GitHub: https://github.com/mwcorley79/smartbulb
Choose “Code””Download Zip”, and save the zip to the Desktop on the laptop
Extract the zip to the desktop

## Slide 41: Secure copy: scp
Use SCP to move the python script (representing the backend) to the Raspberry: smartbulb.py
  Interfaces through the GPIO header, to control the desk lamp
  Open terminal (in Windows or in VSCode)
    start an SSH session with Raspberry Pi:
      Enter command: ssh pi@{teamname}pi.local - replace {teamname} with corresponding team name: example Team: “Viper”  ssh pi@viperpi.local
        Create a new folder to for the python script:
          Issue the command:
            mkdir ~/smartbulb

## Slide 42: Secure copy: scp
Use SCP to move the python script (representing the backend) to the Raspberry: smartbulb.py
  Interfaces through the GPIO header, to control the desk lamp
  Open terminal (in Windows or in VSCode)
    start an SSH session with Raspberry Pi:
      Enter command: ssh pi@{teamname}pi.local - replace {teamname} with corresponding team name: example Team: “Viper”  ssh pi@viperpi.local
        Create a new folder to for the python script:
          Issue the command:
            mkdir ~/smartbulb
    Open another new terminal
      Navigate “smartbulb” project folder and issue the following command:
        scp .\smart_bulb.py username@ip-address:~/smart_bulb

## Slide 43: Install the python MQTT client on Raspberry Pi
pip3 install paho-mqtt=1.6